## Slide 1
VECTO-DEV
14.05.2019
Gearshift Models

## Slide 2: Gearshift Strategies
The following gearshift strategies are implemented in this development release
  AMT
    Classic AMT gearshift strategy (as in the current official VECTO version)
    ACEA/Scania proposed gearshift strategy
    TUG proposed gearshift strategy (FC-based)
  AT
    Classic AT gearshift strategy (as in the current official VECTO version)
    Voith proposed gearshift strategy
    TUG proposed gearshift strategy (FC-based

## Slide 3: Selecting Gearshift Strategy
The Job-Window contains two additional input fields
  Gearshift Strategy on the ‘Driver Model’ tab allows to select from applicable gearshift strategies (AMT/AT)
  On the general tab, an additional file needs to be provided with parameters for the selected shift strategy (details see later)
By default (and in declaration mode) the ‘classic’ VECTO gearshift strategies are used
  These do not need an additional file with the shift parameters (shift lines can be defined in engineering mode for every gear in the gearbox window)
Note: the shift parameter file (and all referenced files) can not be edited in the GUI! Please use a text editor (e.g., notepad++ or notepad) to change certain parameters. You can use the provided examples as starting point

## Slide 4: Classic AMT Gearshift Strategy
Based on upshift and downshift lines which are calculated based on certain parameters of the engine (idling speed, full-load curve)
For details please see the VECTO user manual

## Slide 5: ACEA/Scania AMT Gearshift Strategy
The principle is described in ‘Scania_2018-03-29_Prototype-TCU-VECTO.pdf’ and ‘Scania_2018-06-20_VECTO--Transmission-Control-Unit.pdf’
The documentation of the Matlab implementation is provided in ‘Scania_Transmission Control Unit_Matlab.pdf’
The parameters required for this gearshift strategy are documented in ‘Scania_2018-11-02_Settings-TCU-VECTO.pdf’

## Slide 6: ACEA/Scania AMT Gearshift Strategy Parameter
  StartSpeed
  StartAcceleration
  GearResidenceTime
  Dn_Tq99L_high_min_1
  Dn_Tq99L_high_min_2
  GearRangeUp
  GearRangeDown
  LookBackDriver
  DriverAccelerationLookBackInterval
  DriverAccelerationThresholdLow
  P_card_avg_threshold
  P_card_curr_threshold
  Diff_curr_targ_vel
  EngineSpeedHighDriveOffFactor
  Rating_current_gear
  AccelerationReserveLookup
  ShareTorque99L
  PredictionDurationLookup
  ShareIdleLow
  ShareEngineHigh
The following parameters have to be provided in the shift parameter file (see for example "Examples\Class5_Tractor_4x2_AMT_ACEA\ShiftParameters.vtcu")
Some of the parameters are lookup-tables in CSV format

## Slide 7: TUG FC-Based AMT Gearshift Strategy
The shift strategy is based on gearshift lines for upshift and downshift (similar to the classic VECTO gearshift strategy)
  Allow early upshifts if the current engine operating point is within the gearshift lines if the following criteria are met:
    Upshift: igear+1 <= RatioEarlyUpshiftFC AND
    FCgear +1 < FCgear * Rating_current_gear
  Allow early downshifts if the current engine operating point is within the gearshift lines if the following criteria are met:
    Downshift: igear-1 <= RatioEarlyDownshiftFC AND
    FCgear -1 < FCgear * Rating_current_gear
Purpose of ‘RatioEarlyUpshiftFC’ and ‘RatioEarlyUpshiftFC’: avoid frequent sequential shifts for lower gears (i.e. high gear ratios), FC-based early upshift shall only be possible for higher gears.

## Slide 8: TUG FC-Based AMT Gearshift Strategy
Definition of gearshift lines
  Upshift line
    Vertical line at n_rated
  Downshift line
    Vertical line at 1.1 * n_idle speed up to Tq(n_idle * 1.1) * 0.98
    Engine full-load curve -2% between n_idle and n_tq_99
    Vertical line at n_tq_99
    n_tq_99: lowest engine speed where the engine’s full-load curve reaches 99% of the max. torque

## Slide 9: TUG FC-Based AMT Gearshift Strategy
The following parameters have to be provided in the shift parameter file (see for example "Examples\Class5_Tractor_4x2_AMT_TUG\ShiftParameters.vtcu")
  Rating_current_gear
  RatioEarlyDownshiftFC
  RatioEarlyUpshiftFC

## Slide 10: Classic AT Gearshift Strategy
Based on downshift (pre-shift) and upshift (post-shift) lines
For details please see the VECTO user manual
cont.

## Slide 11: Voith AT Gearshift Strategy
The idea is described in ‘2019_03_25_New_gear_shift_logic_for_Vecto.pdf’, including documentation of the Matlab model
  Limitation: not tested for gearboxes with 2 torque converter gears
cont.

## Slide 12: Voith AT Gearshift Strategy
The following parameters have to be provided in the shift parameter file (see for example "Examples\CityBus_AT_GSVoith\ShiftParameters.vtcu")
LoadStageShiftLines contains the upshift and downshift lines for all load stages. An example is given "Examples\CityBus_AT_GSVoith\GearshiftLinesVoith.vgsv“. Details on the LoadStageShiftLines are provided on the next page
LoadStageThresholdsUp and LoadStageThresholdsDown is a string wit the thresholds for determining the individual thresholds, separated by semicolons (;) – see example
  LoadStageShiftLines
  LoadStageThresoldsUp
  LoadStageThresoldsDown

## Slide 13: Voith AT Gearshift Strategy
LoadStageShiftLines: compared to the documentation provided by Voith, VECTO uses a more general approach for defining the shift lines
  Shift lines have to be defined for every load stage
  For every load-stage, an upper and lower shift line is defined for downhill (-5%), level (0%), and uphill (+5%)
    The shift speed is interpolated between upper and lower bound
    If no interpolation is intended, set the upper and lower bound shift line to the same values
  For both, the upper and lower bound shift lines, the shift speed for amin and amax have to be defined
    For a vertical shift line, set amin and amax to the same value
  In order to simplify the LoadStageShiftLines file, VECTO uses the following rules in case no value is provided in the input file
    The lower bound shift speeds for amax have to be provided in any case (downhill, level, uphill)
    If the lower bound shift speeds for amin are missing, the lower bound shift speeds for amax are used
    If the upper bound shift speeds for amax are missing, the values from the lower bound shift lines for amax are used
    If the upper bound shift speeds for amin are missing, either amax from the upper bound or amax from the lower bound is used

## Slide 14: Voith AT Gearshift Strategy
LoadStageShiftLines: Example upshift 1 -> 2, load stage 1; values for amin
shift , LoadStage , n_dh_amax_lower , n_level_amax_lower , n_uh_amax_lower , n_dh_amin_lower , n_level_amin_lower , n_uh_amin_lower , […]
1-2 , 1 , 650 , 680 , 725 , , , , […]
a
n
amin
amax
680
0% slope

## Slide 15: Voith AT Gearshift Strategy
LoadStageShiftLines: Example upshift 1 -> 2, load stage 4
shift , LoadStage , n_dh_amax_lower , n_level_amax_lower , n_uh_amax_lower , n_dh_amin_lower , n_level_amin_lower , n_uh_amin_lower , n_dh_amax_upper , n_level_amax_upper , n_uh_amax_upper , n_dh_amin_upper , n_level_amin_upper , n_uh_amin_upper
…
1-2 , 4 , 650 , 680 , 725 , 670 , 700 , 745 , , , , , ,
…
a
n
amin
amax
680
0% slope
700

## Slide 16: Voith AT Gearshift Strategy
LoadStageShiftLines: Example upshift 1 -> 2, load stage 5
…shift , LoadStage ,[…], n_level_amax_lower , […], n_level_amin_lower , […], n_level_amax_upper , […], n_level_amin_upper , […]
1-2 , 5 , […], 680 , […], 700 , […], 700 , […], 720 , […]
…
a
n
amin
amax
680
0% slope
700
720
Resulting shift line

## Slide 17: TUG FC-Based AT Gearshift Strategy
The shift strategy is based on gearshift lines for upshift and downshift (similar to the classic VECTO gearshift strategy) and uses the same principle as the FC-based AMT gearshift strategy
  Allow early upshifts if the current engine operating point is within the gearshift lines if the following criteria are met:
    Upshift: igear+1 <= RatioEarlyUpshiftFC AND
    FCgear +1 < FCgear * Rating_current_gear
  Allow early downshifts if the current engine operating point is within the gearshift lines if the following criteria are met:
    Downshift: igear-1 <= RatioEarlyDownshiftFC AND
    FCgear -1 < FCgear * Rating_current_gear
Limitation: not applicable for gearboxes with 2 torque converter gears at the moment

## Slide 18: TUG FC-Based AT Gearshift Strategy
Gearshift lines can be provided as .vgbs file in the gearbox dialog for every gear
In case no gearshift lines are provided, the following shift lines are used
  Upshift line
    Vertical line at n_rated, converted to post-upshift speed via the transmission ratios
  Downshift line
    Vertical line at 1.1 * n_idle speed up to Tq(n_idle * 1.1) * 0.98
    Engine full-load curve -2% between n_idle and n_tq_99
    Vertical line at n_tq_99
    n_tq_99: lowest engine speed where the engine’s full-load curve reaches 99% of the max. torque

## Slide 19: VECTO Outputs
Depending on the selected gearshift strategy, the .vmod file contains additional columns, e.g., the calculated load stage for the AT-Voith proposal, or several intermediate results for the ACEA/Scania proposal
The .vsum file contains an additional column indicating the used gearshift strategy