## Slide 1
VECTO 4.x
Release Notes

## Slide 2
VECTO 0.11.1.3382 Development Version
03.11.2023
Release Notes

## Slide 3: VECTO 3rd Amendment Development Version 03.11.2023
Changes
  Enabled the usage of multiple Fuel Cell Systems (FCS)
    Up to two FCS Strings
    Up to three FCS in each FCS String
  New naming convention:
    FCS: Single Fuel Cell System, described with MassFlowMap (.vfcm) and power limits container in the Fuel Cell System File (.vfcc).
    FCS String: Defined in the .vveh file, can contain up to three identical FCS
    CFCS: Composite Fuel Cell System, a virtual fuel cell system containing up to two FCS String.
  Changes in input files due to new naming convention
  Optimized power distribution among FCS Strings and between individual FCS inside a string.(Explained in more detail in the user manual)
  Allow operating a FCS below its minimum power via time splitting
  Removed On/Off – Hysteresis
  Removed Gradient Power Change

## Slide 4
VECTO 0.11.0.3193 Development Version
29.09.2023
Release Notes

## Slide 5: First VECTO beta release for the 3rd Amendment H2 Internal Combustion Engines
TUG

## Slide 6: H2 ICE
New fuel types implemented „H2 PI“ and „H2 CI“ (i.e. H2-Diesel dual-fuel)
Well-known ICE input data structure unchanged, no new elements
Fuel characteristics used

## Slide 7: First VECTO beta release for the 3rd Amendment Fuel Cell Hybrid Vehicles (FCHV)
TUG

## Slide 8: Fuel cell hybrid vehicles (FCHV) – Op. strategy (1/5)
FCHV generic operation strategy (Charge Sustaining Mode) implemented as presented in TF FCS #15 with following basic principle:
  Maximum phlegmatisation of FCS by operation strategy
  FCS needs to provide average electric power demand over longer horizon
  Longest possible averaging horizon depends on battery size and specific vehicle-cycle combination  The smaller the battery or the greater the electric energy demand of the vehicle, the smaller the averaging horizon will get leading to a more dynamic operation of the FCS.

## Slide 9: Fuel cell hybrid vehicles (FCHV) – Op. strategy (2/5)
Basic approach for implementation of FCS operation in “CS” Mode in 4 steps
  Pre-simulation run as PEV to determine electric power demand for propulsion and auxiliaries
    Power limit of “special” battery defined as sum of respective maximum powers (BAT + FCS)
  Resulting total electric power from step 1 will be averaged over a certain fixed window size which is distance based (details next slide)
    Buffering of energy is limited by battery size, SOC limits min/max are not allowed to be exceeded
    Using largest possible window size without violating SOC limits in any window
    Adaption of start SOC to specific mission in order to maximize usage of battery as buffer
  Actual simulation run as FCHV in-the-loop where FCS is operated following a fixed power trace to cover average electric power demand determined from pre-processing in step 2 (battery covers instantaneous deviations from average electric power demand)
  ΔSOC correction in post-processing to account for small deviations from neutral SOC behaviour over cycle (e.g. variations in auxiliary power, small deviations in battery losses etc.)

## Slide 10: Fuel cell hybrid vehicles (FCHV) – Op. strategy (3/5)
Averaging and window size explained (1/2)
  The averaging window is placed distance-symmetrically over each actual time step from the pre-simulation
  Window size is determined by total distance within window
distance
=
time
t
t+1
t+1-j
t-i
t+2
t+i
t+1+j
window @ t
window @ t+1
window @ t+2
t+2+k
t+2+k
distance
=

## Slide 11: Fuel cell hybrid vehicles (FCHV) – Op. strategy (4/5)
Averaging and window size explained (2/2)
  Maximum window size is given by complete cycle, thus cycle is concatenated 3 times in a row
  For time steps near the beginning or end of the cycle, the windows expand over the actual cycle and continue at the adjacent parts at the end or beginning.
time
previous copy of cycle
actual cycle
subsequent copy of cycle
speed
window at beginning of cycle
window in the middle of cycle
window at end of cycle

## Slide 12: Fuel cell hybrid vehicles (FCHV) – Op. strategy (5/5)
Actual simulation run as FCHV and applicable boundary conditions
  In case average power demand over total cycle is higher than FCS maximum power:  defined error message and simulation is aborted (vehicle configuration not reasonable for this mission, should not occur in practice)
  In case average power in a certain timestep is lower than FCS minimum power:  FCS is switched off  missing energy from FCS for those timesteps will be accounted for in post-processing via ΔSOC correction

## Slide 13: Fuel cell hybrid vehicles (FCHV) – VECTO features (1/5)
New powertrain type of FCHV added to Job Editor

## Slide 14: Fuel cell hybrid vehicles (FCHV) – VECTO features (2/5)
FCS to be parameterized via specific „Fuel Cell System“ tab in „Vehicle“ editor
Power gradient limits change in FCS power over time
On/off-Hysteresis is minimum time that FCS stays off or on after state change occurs  not required anymore after insights gained during work on implementation of multiple FCS

## Slide 15: Fuel cell hybrid vehicles (FCHV) – VECTO features (3/5)
FCS to be parameterized via specific „Fuel Cell System“ tab in „Vehicle“ editor
Double-click or „+“
Limited to 1
for this release
Max / min power limits operation range of FCS component
FCS mass flow map needs to cover the indicated range

## Slide 16: Fuel cell hybrid vehicles (FCHV) – VECTO features (4/5)
FCS to be parameterized via specific „Fuel Cell System“ tab in „Vehicle“ editor
Input data structure for FCS H2 mass flow map
CSV file format
  1st column: Electric power output of FCS in [kW]
  2nd column: H2 mass flow in [g/h]
FCS component efficiency should also include DC/DC converter (as this is part of component test procedure)!
Example data

## Slide 17: Fuel cell hybrid vehicles (FCHV) – VECTO features (5/5)
Parameterization of auxiliaries for FCHV
  Electric power demand of auxiliaries for both, lorries and buses, need to be parameterized via the “Bus Auxiliaries” GUI window
Demand during vehicle driving
Demand during vehicle standstill
INFO: Electric aux power demand is calculated by multiplying the specified current values by a voltage of 28.3V

## Slide 18: FCHV – Examples for generic operation strategy (1/5)
Exemplary results for VECTO Group 2 12-ton rigid lorry (9.5 ton actual mass) on following slides
Simulation in VECTO Urban Delivery Cycle
  Average electric power demand around 22 kW
FCHV powertrain specifications:
  100 kW FCS max power
  following variants of battery:
    5 kWh
    10 kWh
    20 kWh
Resulting speed profile was exactly the same for all different configurations

## Slide 19: FCHV – Examples for generic operation strategy (2/5)
The lower the buffer size, the more dynamic the FCS operation gets
Exactly same speed profile for all variants
Averaging window sizes determined:
  5 kWh: 6 km
  10 kWh: 37.5 km
  20 kWh: 100 km
5 kWh
10 kWh
20 kWh
Fuel cell power for different battery sizes

## Slide 20: FCHV – Examples for generic operation strategy (3/5)
Battery covers instantaneous deviations from average electric power demand
Average electric power demand (i.e. FCS power) constant for the setting shown with 20 kWh REESS size
Battery power
Fuel cell power

## Slide 21: FCHV – Examples for generic operation strategy (4/5)
Using largest possible window size without violating SOC limits in any window  maximizing of battery buffer usage
Exactly same speed profile for all variants
SOC limits are Engineering settings, no connex to generic limits used in Declaration Mode
5 kWh
10 kWh
20 kWh
Upper SOC limit
Lower SOC limit
SOC for different battery sizes

## Slide 22: FCHV – Examples for generic operation strategy (5/5)
Adaption of start SOC to specific mission in order to maximize usage of battery as buffer (detail from previous graph)
Exactly same speed profile for all variants
5 kWh
10 kWh
20 kWh
Adapted start SOC
SOC for different battery sizes

## Slide 23: Fuel cell hybrid vehicles (FCHV) - Comments
Release to be distributed via VECTO-DEV mailing list end of September
  Basic description of FCHV features will also be added to VECTO release notes
  Some example vehicles will be provided
Current release restricted to one single FCS component
Updated release end of October will be able to handle:
  multiple FCS configurations as presented in TF FCS #17
    Maximum 2x3 configuration i.e. 2 different FCS with a maximum number of 3 identical systems for each of the 2 different ones
  Special provisions for handling power demands below minimum FCS power
  IMC feature combined with FCHV

## Slide 24: First VECTO beta release for the 3rd Amendment Vehicles with In-Motion Charging Features
TUG

## Slide 25: Vehicles with In-Motion Charging (IMC) features (1/11)
One of the tasks of the pre-development project for the 3rd Amendment was to analyse different systems for in-use charging of electric vehicles
  State of the art
  Relevance and possible paths of implementation to Regulation (EU) 2017/2400
  Functional prototype
The analyses and proposals for (1) and (2) were presented and discussed with stakeholders in five stakeholder meetings (Oct 2021, Dec 2021, Jan 2022, Jun 2022 and Sept 2022).
The following slides summarise the most important principles and present the functional prototype

## Slide 26: Vehicles with In-Motion Charging (IMC) features (2/11)
Reference point for results regarding electric energy consumption
Principle applied already for the 2nd amendment
Consequences for the 3rd amendment
  Stationary charging: minor improvements to the Annex (max. charging power)
  In-motion charging: Requires model extension and separate provisions in the Annex

## Slide 27: Vehicles with In-Motion Charging (IMC) features (3/11)
Modelling in VECTO - Overview
  Driving with “direct feed” incorporated to simulations of “charge depleting” mode by postprocessing (no additional sim time, no additional definitions etc.) (DECL)  higher utility factor / share of electric driving for OVC-HEV  (slightly) lower battery internal losses
  Charging of batteries by IMC handled by postprocessing (DECL)  higher utility factor / share of electric driving for OVC-HEV
  Impact on air drag incorporated to in-the loop simulation via a mission average share “active” (which applies either to motorway sections or to the total cycle) (ENG, DECL)
  No direct influence on the “electric ranges", i.e. these are also only calculated on the basis of the usable battery capacity (DECL)
DECL / ENG: Effect visible in Declaration Mode / Engineering Mode
Report with detailed documentation to be published soon

## Slide 28: Vehicles with In-Motion Charging (IMC) features (4/11)
Modelling in VECTO – Calculations of electric energy consumption at battery terminals
Calculation examples see Task3_Masterexcel_OVC_IMC.xlsx as distributed with ppt Report with detailed documentation to be published soon
Lila terms: new elements introduced for IMC modelling

## Slide 29: Vehicles with In-Motion Charging (IMC) features (5/11)
Modelling in VECTO – Current proposals for Declaration Mode
Lila: to be worked out for the 3rd amendment
In-motion charging “technology” | Relevance |  |  | Proposal for definition in Regulation (EU) 2017/2400
 | Heavy lorries | Heavy buses | Medium lorries | 
Overhead pantograph | Yes | Yes | No | Vehicle equipped with overhead pantograph for connection with overhead catenary infrastructure as regulated by standard tbd and which is not overhead trolley.
Overhead trolley | No | Yes | No | Vehicle equipped with poles for connection with overhead catenary infrastructure as regulated in Annex 12 to UN Regulation 107 revision 8.
Ground-rail | Yes1 | Yes1 | Yes1 | Charging technology that conductively transfers the electrical energy to the vehicle through rails embedded in or on top of the road surface.
Wireless | Yes1 | Yes1 | Yes1 | Charging technology that inductively transfers the electrical energy to the vehicle through devices embedded in or on top of the road surface providing magnetic fields as they are specified IEC 61980.
1 Only Potential niche applications are conceivable.

## Slide 30: Vehicles with In-Motion Charging (IMC) features (6/11)
Modelling in VECTO – Proposal for IMC infrastructure availability
Overhead - Pantograph
Overhead - Trolley

## Slide 31: Vehicles with In-Motion Charging (IMC) features (7/11)
Modelling in VECTO – Proposal for IMC infrastructure availability
Ground rail + Wireless

## Slide 32: Vehicles with In-Motion Charging (IMC) features (8/11)
Modelling in VECTO – Further proposed assumptions
  Battery charging during mission
    50% of usable battery capacity via “SOC lift” by IMC
    No further stationary charging
  Air drag
    Considered only for “Overhead – pantograph”
    ΔCdxA = 0.6 m² for the shares in the mission where IMC is available

## Slide 33: Vehicles with In-Motion Charging (IMC) features (9/11)
Inputs in Graphical User Interface (ENG)
Attention!
Working with ENG mode simulations for IMC features requires detailed knowledge of the proposed approach (mainly for developers)
For checking of regulatory impact DECL mode testing recommended!
New tab in “VEH Editor” for HEV and PEV vehicles

## Slide 34: Vehicles with In-Motion Charging (IMC) features (10/11)
Inputs in Graphical User Interface (DECL)
Dropdown Menu with pre-defined technologies
  None
  Overhead Pantograph
  Overhead Trolley
  Ground Rail
  Wireless

## Slide 35: Vehicles with In-Motion Charging (IMC) features (11/11)
Example vehicle models will be distributed with the release (located in “\Generic vehicles”)
Base specs example models
  Group 5 / HEV P2 / OVC: Pcont_EM: 200kW | EReess: 120kWh nominal
  Group 5 / PEV: Pcont_EM: 325kW | EReess: 170kWh nominal
Example results: Long haul with rep payload Comparison results “w/o” and “w/” pantograph with similar other vehicle specs like mass
  Group 5 / P2 / OVC w/o pantograph: UF = 0.149; CO2weighted = 692.2 g/km
  Group 5 / P2 / OVC w/ pantograph: UF = 0.660; CO2weighted = 347.1 g/km  -50% CO2
  Group 5 / PEV w/o pantograph: ECel = 1.262 kWh/km
  Group 5 / PEV w/ pantograph: ECel = 1.297 kWh/km  +2.8% ECel