## Slide 1: Adding New Cycle or Mission Profile for Vehicle Types in BharatVECTO
Process Guide with System Architecture and Impact Analysis
VECTO Development Team

## Slide 2: What is BharatVECTO?
VECTO: Vehicle Energy Consumption Calculation TOol
Official EU vehicle simulator for Heavy Duty Vehicles (HDVs)
Certifies CO₂ emissions and fuel consumption
Mandatory for trucks since January 2019 (EU Regulation 2017/2400)
Uses standardized driving cycles to simulate real-world conditions
Written in C# / .NET Framework 4.5+

## Slide 3: Understanding Driving Cycles & Mission Profiles
Driving Cycle: Standardized speed-time or speed-distance profile
Represents typical vehicle operation patterns
Mission Profile: Operational scenario for specific vehicle use cases
Components: Speed, gradient, distance, stopping times, auxiliary loads
Purpose: Ensure consistent, reproducible testing for regulatory compliance
Different vehicle types and missions use different cycles

## Slide 4: Mission Types in VECTO
TRUCK MISSIONS:
• LongHaul - Long-distance freight
• RegionalDelivery - Regional distribution
• UrbanDelivery - City delivery
• MunicipalUtility - Municipal services
• Construction - Construction sites
BUS/COACH MISSIONS:
• HeavyUrban - Dense city routes
• Urban - City bus operations
• Suburban - Suburban routes
• Interurban - Inter-city connections
• Coach - Long-distance services

## Slide 5
System Architecture Overview
┌──────────────────────────────────────────────────────┐ │ VECTO Application (GUI/Console) │ └─────────────────────┬────────────────────────────────┘ │ ▼ ┌──────────────────────────────────────────────────────┐ │ VectoRunDataFactoryFactory │ │ (Routes to appropriate factory based on vehicle) │ └─────────────────────┬────────────────────────────────┘ │ ┌─────────────┴─────────────┐ ▼ ▼ ┌───────────────────┐ ┌───────────────────────────┐ │ Declaration Mode │ │ Engineering Mode Factory │ │ Factory │ │ │ └────────┬──────────┘ └───────────────────────────┘ │ ▼ ┌──────────────────────────────────────────────────────┐ │ DeclarationCycleFactory │ │ (Retrieves default cycles from embedded resources) │ └─────────────────────┬────────────────────────────────┘ │ ▼ ┌──────────────────────────────────────────────────────┐ │ Embedded Mission Cycle Resources (.vdri files) │ │ VectoCore/Resources/Declaration/MissionCycles/ │ └──────────────────────────────────────────────────────┘

## Slide 6: Key Components & Their Relationships
1. DeclarationCycleFactory: Retrieves default cycles, caches for performance
2. DrivingCycleDataReader: Parses .vdri files, auto-detects cycle type
3. VectoRunDataFactoryFactory: Factory pattern routing to vehicle-specific factories
4. Mission.cs: Defines mission properties (loads, passengers, trailers)
5. MissionType enum: Defines all available mission types
6. Embedded Resources: Cycle files stored as embedded resources in assembly

## Slide 7: Process Overview: Adding a New Cycle (8 Steps)
Step 1: Define cycle parameters and mission requirements
Step 2: Create cycle file (.vdri format) with proper headers
Step 3: Embed resource or add to file system
Step 4: Update factory classes (if adding new mission type)
Step 5: Write comprehensive unit tests
Step 6: Run integration tests with generic vehicles
Step 7: Validate results against specifications
Step 8: Deploy with documentation and release notes

## Slide 8
Steps 1-2: Define & Create
Step 1: Define Parameters • Cycle Type: DistanceBased, EngineOnly, MeasuredSpeed, VTP, PTO • Mission Type: Choose from existing or create new • Data Requirements: speed, gradient, distance, stops • Regulatory compliance requirements Step 2: Create Cycle File (.vdri) Example Distance-Based format: <s>,<v>,<grad>,<stop> 0,0,0,10 100,30,0,0 500,50,0.005,0 1000,70,0.01,0 1500,0,0,15 Headers: <s>=distance(m), <v>=speed(km/h), <grad>=gradient(rad), <stop>=stop time(s)

## Slide 9: Steps 3-4: Embedding Resource & Updating Factory
Step 3 - Embed as Resource:
• Add file to: VectoCore/Resources/Declaration/MissionCycles/
• Set Build Action to 'Embedded Resource' in Visual Studio
• Naming: {MissionType}.vdri (e.g., LongHaul.vdri)
Step 4 - Update Factory (if NEW mission type):
• Update MissionType enum in VectoCommon/Models/
• Update MissionTypeHelper with display name
• DeclarationCycleFactory auto-detects by convention

## Slide 10: Cascading Effects: Code Changes Required
Primary Changes:
• MissionType enum addition triggers compilation across entire solution
• All switch statements on MissionType need updating (compiler enforced)
• Factory methods must handle new mission type
Secondary Effects:
• GUI components: dropdown lists, mission selection dialogs
• Report generators: need to format new mission results
• Validation logic: weighting factors, load combinations
• XML serialization/deserialization schemas

## Slide 11
Integration with Simulation Components
Cycle Integration with Simulation Pipeline: ┌──────────────┐ ┌──────────────────┐ ┌─────────────┐ │ Cycle File │───>│ DrivingCycleData │───>│ Simulation │ │ (.vdri) │ │ Object │ │ Engine │ └──────────────┘ └──────────────────┘ └──────┬──────┘ │ ┌──────────────────────────────────────────┘ │ ▼ ┌────────────────────────────────────────────────────┐ │ Simulation Components: │ │ • PowertrainBuilder: configures powertrain │ │ • VehicleModel: applies vehicle parameters │ │ • EngineModel: processes speed/load from cycle │ │ • TransmissionModel: gear selection per cycle pt │ │ • AuxiliaryModel: auxiliary loads from cycle │ │ • ResultCalculator: computes CO2, fuel, energy │ └────────────────────────────────────────────────────┘

## Slide 12: Step 6: Integration Testing Requirements
Test Categories:
• Unit Tests: Cycle file parsing, header detection, data validation
• Factory Tests: Cycle retrieval, caching, multiple mission handling
• Integration Tests: Full simulation runs with generic vehicles
• Regression Tests: Ensure existing cycles remain unaffected
Testing Tools:
• NUnit framework for unit and integration tests
• VECTO GUI for manual validation
• Generic vehicle files in 'Generic Vehicles/Declaration Mode/'

## Slide 13: Step 7: Validation & Impact Analysis
Physical Validation:
• Speed values achievable for vehicle type
• Gradient values within realistic ranges (-10% to +10%)
• Energy balance correctness
Regulatory Compliance:
• Meets EU certification requirements
• Proper documentation and audit trail
Impact Assessment:
• Backwards compatibility with existing vehicles
• Performance impact on simulation runtime
• Changes to result file formats (.vres, .vsum)

## Slide 14: Cascading Effects: Potential Impacts Summary
CODE IMPACTS:
• Enum additions require recompilation
• Switch statement updates
• GUI updates for new missions
• XML schema changes
• Report template updates
DATA IMPACTS:
• New embedded resources
• Assembly size increase
• Cache initialization time
TESTING IMPACTS:
• All affected tests must pass
• New test cases required
• Generic vehicle updates
DEPLOYMENT IMPACTS:
• Version number update
• Release notes documentation
• User manual updates
• Training material revisions
• Stakeholder communication

## Slide 15: Best Practices & Common Pitfalls
DO:
✓ Validate cycle data thoroughly before embedding
✓ Write comprehensive unit tests for all changes
✓ Document changes in code comments and guides
✓ Test with multiple vehicle configurations
✓ Use version control and code reviews
DON'T:
✗ Skip validation or testing steps
✗ Break backwards compatibility without documentation
✗ Use unrealistic speed or gradient values
✗ Forget to update MissionTypeHelper for display names

## Slide 16
Troubleshooting Common Issues
Common Issues and Solutions: Issue: Resource not found exception Solution: Verify Build Action = "Embedded Resource" and correct resource naming convention Issue: Cycle type detection fails Solution: Check header format uses angle brackets: <s>,<v> Ensure headers are case-insensitive Issue: Validation errors during parsing Solution: Verify monotonic distance/time values Check for realistic speed/gradient ranges Issue: Factory returns null for new mission Solution: Ensure MissionType enum updated and .vdri file named exactly as enum value (case-sensitive) Issue: Integration tests fail Solution: Check generic vehicle compatibility Verify all simulation components initialized

## Slide 17
File Locations Reference
Key File Locations: Component Path ───────────────────────────────────────────────────────── Cycle Factory VectoCore/Models/Declaration/ IDeclarationCycleFactory.cs Mission Type Enum VectoCommon/Models/ MissionType.cs Cycle Data Model VectoCore/Models/SimulationComponent/ Data/DrivingCycleData.cs Cycle Reader VectoCore/InputData/Reader/ComponentData/ DrivingCycleDataReader.cs Embedded Resources VectoCore/Resources/Declaration/ MissionCycles/*.vdri Unit Tests Testing/UnitTests/Vecto UnitTests/ TestCases/ComponentReader/ Integration Tests Testing/IntegrationTests/ VECTO IntegrationTests/ Generic Vehicles Generic Vehicles/Declaration Mode/

## Slide 18: Step 8: Deployment Process
Pre-Deployment Checklist:
☐ All unit tests passing (100%)
☐ Integration tests completed successfully
☐ Code review approved
☐ Documentation updated (user manual, developer guide)
☐ Release notes prepared
Deployment Steps:
1. Update version number in assembly info
2. Clean rebuild in Release configuration
3. Test in staging environment
4. Deploy to production
5. Communicate changes to users and stakeholders

## Slide 19: Summary: Key Takeaways
1. VECTO uses embedded cycle resources for declaration mode missions
2. DeclarationCycleFactory retrieves cycles by convention (MissionType name)
3. Adding cycles requires updates to multiple system components
4. Cascading effects include: enums, factories, GUI, tests, documentation
5. Integration testing is critical - test with generic vehicles
6. Thorough validation ensures regulatory compliance
7. Follow the 8-step process for successful implementation
8. Documentation and code reviews are essential for quality

## Slide 20: Resources & Next Steps
Documentation:
• Full Guide: Documentation/Developer Guide/Adding_Updating_Default_Cycle_Guide.md
• Quick Reference: Documentation/Developer Guide/Cycle_Addition_Quick_Reference.md
• Test Templates: Documentation/Developer Guide/CycleAddition_UnitTest_Template.cs
Support:
• Email: JRC-VECTO@ec.europa.eu
• Repository: https://code.europa.eu/vecto/vecto
Next Steps:
1. Review full documentation guides
2. Set up development environment
3. Practice with existing cycles before adding new ones